## Slide 1: Surveyors Compass
Box with center point
Magnetized Needle
  Lift needle
Blade Sights
Level tubes
Base
  Jacob’s staff
  Tripod

## Slide 2: Magnetic Compasses
Magnetized Needle
  Points North
  Dips down
  Wire wrap
Compass Rose is backwards
Local Attraction

## Slide 3: Magnetic Declination
Longitude – true North
Magnetic North not true
Angular difference – magnetic declination
Varies by place – E or W
Varies with time

## Slide 4: Isogonal Map
Agonic Line
East Declination
West Declination
Annual Drift
Map Date

## Slide 5: Declination in Moorhead
In 1980
  7° E
  Drifting 10’ W/year
Now
  Assume E = (+)
  7° + (-10’/yr)(24 yr) = 3°00’
Use most current map available

## Slide 6: Declination Calc’s
Old survey in Moorhead sets line AB
  Decl then = 11°15’ E
  True = Mag + Decl
    True Az = 141°38’ + 11°15’ = 152°53’
Find True direction now
  Convert to Azimuth
    Mag Az = 141°38’
N
M
  Mag Bearing AB = S38°22’E

## Slide 7: Problem 9-28
1890 Survey
  Decl = 7°00’ E (+)
True = Mag + Decl
  True Az = 134°30’ + 7°00’ = 141°30’
Mag Az Now
  Decl Now = 3°30’ W (-)
N
M
M
  Mag Az = 134°30’
  Mag = True – Decl
  Mag Az = 141°30’ – (-3°30’) = 145°00’