## Slide 1
University of California, Berkeley
Department of Civil and Environmental Engineering
Professor Jasenka Rakas
Kevin Cheng | Ian Tai | Jeff Ma
Zhuo Chen | Steven Chua | Phil Tran
December 06, 2012
Future of DataComm

## Slide 2: The NextGen Vision
A system that is based on satellite navigation and control, digital non-voice communication and advanced networking, and a sharing of decision making between the ground and the cockpit.
Notes: 2
They jointly created a vision for the Next Generation Air Transportation System (NextGen) that would modernize the NAS and take advantage of new automation and technologies to accommodate the expected growth of air transportation.

## Slide 3: NextGen: Improving Efficiency & Capacity
Today’s NAS
NextGen
Ground-based Navigation and Surveillance
Air Traffic Control Communications By Voice
Disconnected Information Systems
Air Traffic “Control”
Fragmented Weather Forecasting
Airport Operations Limited By Visibility Conditions
Forensic Safety Systems
Satellite-based Navigation and Surveillance
Routine Information Sent Digitally
Information More Readily Accessible
Air Traffic “Management”
Forecasts Embedded into Decisions
Operations Continue Into Lower Visibility Conditions
Prognostic Safety Systems
Notes: 3
3
SLIDE #2
Also mention:
Safety is paramount.
Global harmonization is essential.
Environmental stewardship must be a focus.
We understand what must change in order to realize NextGen.
We are working to implement the foundational programs today, and define the future building blocks that enable mid- and far-term operational capabilities.
We have identified timelines and budgets to support them.

## Slide 4: What is Data Comm?
Text-based communication that serves as an enabler for future NextGen concepts
Rough Analogy
Phone Calls : Text Messages
Radio Frequencies : DataComm
Notes: Data Comm is designed around the basic principles listed on this slide:
First, Data Comm builds on the experience gained from CPCLC in Miami, over the Ocean, and through the European Link 2000 program to design a practical approach, implementing Data Communications in an incremental fashion (Data Comm is harmonized with Europe. We are leveraging the same Mode 2 technology being implemented by the Europeans for their initial and follow on data network).
Second, Data Comm is being designed to meet all safety requirements. (Design, performance requirements that are not extensible, we will build to meet Seg Two requirements from outset.)
Third, Data Comm is leveraging existing equipage such as Mode 2 avionics, and program plans include accommodating FANS.
Additionally, the Data Communications Program is working jointly with EUROCAE Working Group 78 through RTCA Special Committee 214 to develop avionics standards that will support all Data Comm capabilities through Segment Two to maximize airspace user benefits. We are expecting SC-214 to become the converged application for Europe and the US since the Europeans have indicated their plans to leverage SC-214 standards in their follow on data link implementation.

## Slide 6: General DataComm Benefits
Reduces controller and pilot workload
Human memory less critical
Increases capacity of radio frequencies
Diminishes error and increases clarity
Presents unique advantages and applications

## Slide 7: Data Comm: Challenges
Heads-down time
Party line loss
Passive readback
No information from tone of clearance/readback
Visual information overlooked?
  Incoming Data Comm on FMS requires paging
    away from current activity
    to get full message
  Aural alert may be insufficient & indistinguishable from other alerts
Mixed voice/Data Link may distract from one other
Controller must track multiple comms w/ delayed response times

## Slide 8: Methodology: Our Approach
Literature Review
Human-factor via interviewing
Current uses of DataComm
Future of Data Comm
Generation of Innovative Ideas

## Slide 9: Innovative Idea Generation
Members reviewed current uses and literature existing and developed ideas of future application utilizing DataComm, for Tower, TRACON, and En Route regions
Collaborative idea generation for DataComm applications. With support and assistance from NASA, generation of brand new ideas, “out-of-the-box” or “crazy” ideas.
Ideas Currently Developed:
Automated Tower Systems (ATS)
Deep Flight Deck Integration (DFDI)
Biomimicry – Flight Formation
Segregated Information Broadcast (SIB)
Automated Aircraft Reporting (AAR)
Notes: Result may be due to different multiple processing “resources” associated with visual and auditory processing

## Slide 10: Automated Tower System (ATS)
By: Ian Tai

## Slide 11: Introduction
 Without a tower or controller, these tasks fall to pilots themselves.
  Air Traffic Control (ATC) Duties
  Single point of communication
  Sequencing, takeoffs, landings, taxiing
  “…provide safe, orderly, expeditious flow of traffic” (FAA)
Automated Tower System (ATS)  Motivation?

## Slide 12: Non-Towered Airport Protocol
Facility at Airport
Frequency Use
Communication/Broadcast Procedures

## Slide 13: Non-towered Consequences
Congestion on CTAF
Lower situational awareness
No centralized communication
VFR for takeoff, landing, taxiing, sequencing
Multiple aircraft and aircraft type
Landings: same runway, different directions

## Slide 14
Via DataComm
Via DataComm
Air Side
Ground Side

## Slide 15: Detailed Flow Chart

## Slide 16: Requisites for Implementation
Aircraft
Control Tower
Hardware for cockpit
  DataComm compatible
Software for equipment.
Ability to read transmissions from Control tower and display instructions
Hardware for Control Tower, able to receive and relay DataComm messages
Software for control tower
Ability to input, process, and output data
Establish Standard Procedures and Protocol for ATS

## Slide 17: Benefits of Automated Towers
Safety Benefits:
  Streamlined situational awareness
  Centralized communication, diminishes errors
  Decreases congestion
  Economical: ATS vs. building a tower or staffing
  Diminishes human error

## Slide 18: Summary
Automated Tower System, can directly use DataComm
Benefits: Safety and economical
Application to houred towers or non-towered airports
Future application to large airports

## Slide 19: Data Link Deep Flight Deck Integration (DLDFDI)
By: Kevin Cheng

## Slide 20: Background
Data Communications is primarily interacted with through the Multi-function Control and Display Unit (MCDU)

## Slide 21: Background
Pros
Cons
Accurate Readback
Least disruptive to ongoing tasks
Information permanence
Diverts attention from visually critical areas
Chance of “forgetting” to resume task prior to ATC message
Decreased situational awareness
Data Communications  “Visual Attention Costs”

## Slide 22: Background
Methods were introduced to eliminate or reduce the cost of visual attention by Data Communications
Many studies performed on Data Communications aim to address the costs of visual attention diverted away from the instrument panel
Introduced studies for a redundant text-voice format
“Cross-modal (auditory-visual) presentation yielded a more efficient performance than did intramodal (visual-visual) display information presentation.”
John R. Helleberg & Christopher D. Wickens (2003): Effects of Data-Link Modality and Display Redundancy on Pilot Performance: An Attentional Perspective, The International Journal of Aviation Psychology, 13:3, 189-210
Notes: Result may be due to different multiple processing “resources” associated with visual and auditory processing

## Slide 23: Problem, Engagement, and Methodology
Lengthy readbacks can “step” on actual transmissions from ATC
Reducing audio clutter is an objective of Data Communications
Cross-modal (auditory-visual) display of communication poses a problem
Data Communications  “Auditory Clutter”
“humans could only differentiate between five different sounds in a cockpit”

## Slide 24: Problem, Engagement, and Methodology
“Auditory Clutter”
“Visual Attention Costs”
Data Communications Today
Our Approach:
Find a method of data communication transmission presentation that doesn’t increase audio clutter in cockpit and focuses attention on flight critical information

## Slide 25: Problem, Engagement, and Methodology
Primary Flight Display
Navigation Display
Heads Up Display
Our Solution: Integrate data communication transmission into the flight critical visual areas to keep more focus on ongoing task
Deep Flight Deck Integration (DFDI)

## Slide 26: Deep Flight Deck Integration (DFDI)
Notes: Present the information on the screen

## Slide 27: DFDI solves Data Communication shortfalls
DFDI
Cons
Diverts attention from visually critical areas
Chance of “forgetting” to resume task prior to ATC message
Decreased situational awareness
Refocuses attention towards visually critical areas
Decreases chance of “forgetting” to resume ongoing task
Increases situational awareness
Notes: Increases situational awareness

## Slide 28: DFDI Demonstration

## Slide 29: DFDI Benefits
Reduces “Visual Attention Costs”
Does not add to auditory clutter in the cockpit
Instructions displayed on the PFD and ND
Fewer memory and focus demands
Improves situational awareness

## Slide 30: DFDI as a Future Concept Enabler
Automated Air Traffic System
Remote Aircraft Control
Phase 1:
Basic DFDI
Phase 2:
DFDI with reporting capabilities
Phase 3:
DFDI with automated conflict solving abilities
Phase 4:
Automated airspace sector management with DFDI
Notes: NASA has its own objective  automate the entire air traffic system in addition to being able to control aircraft from the ground like a strategian
Of course, that’s not going to happen overnight  also, I’m a pilot too and I have issues with that cause that’ll put me out of a job…
But there are phases towards that goal
Here, to illustrate DFDI as a Future Concept Enabler, I am compounding DFDI and its evolution of capabilities to the phases that NASA will take to ultimately automate airspace.

## Slide 31: Phase 1: Basic DFDI
NASA Objective | Reduce communication congestion
DFDI Capabilities | ATC Instructions integrated into the avionics
Communication Abilities | GroundAir

## Slide 32: Phase 2: DFDI With Reporting Capabilities
NASA Objective | Reduce communication congestion Improve predictability
DFDI Capabilities | ATC Instructions integrated into the avionics DFDI reports maneuver completion
Communication Abilities | GroundAir AirGround
Notes: We evolve DFDI to have reporting capabilities…once the pilot finishes the maneuver, DFDI reports this fact back to the controllers so they know that the sequence is done.

## Slide 33: Phase 3: DFDI With Conflict Solving Abilities
NASA Objective | Reduce communication congestion Improve predictability Detect and solve conflicts automatically
DFDI Capabilities | ATC Instructions integrated into the avionics DFDI reports maneuver completion DFDI auto-solves trajectory conflicts
Communication Abilities | GroundAir AirGround Reports and suggests maneuvers to controller
Notes: If NASA’s next objective is to detect and solve conflicts automatically, then DFDI will evolve and also assist with auto-solving trajectory conflicts…
For example, through VDL Mode 4, aircraft will talk to each other and figure out how best they will solve their own conflicts. The controller takes a passive role and only monitors this sequence.

## Slide 34: Phase 4: DFDI With Automated Sector Management Abilities
NASA Objective | Reduce communication congestion Improve predictability Detect and solve conflicts automatically Automate airspace sectors
DFDI Capabilities | ATC Instructions integrated into the avionics DFDI reports maneuver completion DFDI auto-solves trajectory conflicts DFDI manages airspace
Communication Abilities | GroundAir AirGround Reports and suggests maneuvers to controller AirAir/Ground communication
Notes: Lastly, as we get closer to airspace automation, we expand the last idea into a whole airspace sector.
Aircraft will talk to each other and generate full trajectories on how they will navigate the airspace. DFDI will help with that when it provides suggestions on the avionics.

## Slide 35: Biomimicry – Formation Flight
By: Steven Chua

## Slide 36
Source: Airbus
Notes: Flying at a given spot in the wake of another aircraft can decrease
induced drag

## Slide 38
Source: Airbus

## Slide 39
Source: Airbus

## Slide 40: Formation Flight Benefits
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Source: Greg Larson
Source: Andrew Ning
Notes: Why now?
– New advances in software and GPS have enabled position- keeping
• NASA AFF program
– World air cargo traffic growing on average 6.4% per year in the next 20 years
• Asian market growing at 10.3%
– Fuel prices increasing (44% over the past year) • Demand for technology to lower fuel costs • Fuel costs normally 12-18% of total airline costs

## Slide 41: Formation Flight Benefits
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Air Cargo Carriers
Cargo carriers save money
Reduced prices capture market share, increase profit
Increased range reaches additional markets, more profit
Notes: For Air cargo carriers:
– Cargo carriers save money
– Reduced prices capture market share, increase profit
– Increased range reaches additional markets, more profit

## Slide 42: Formation Flight Benefits
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Commercial Airlines
Reduces air traffic en-route
Will lead to autonomous formation take-off and landing to reduce airport congestion.
Notes: For Air cargo carriers:
– Cargo carriers save money
– Reduced prices capture market share, increase profit
– Increased range reaches additional markets, more profit

## Slide 43: Formation Flight Benefits
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Commercial Airlines
Reduces air traffic en-route
Will lead to autonomous formation take-off and landing to reduce airport congestion.
Notes: For Air cargo carriers:
– Cargo carriers save money
– Reduced prices capture market share, increase profit
– Increased range reaches additional markets, more profit

## Slide 44: Formation Flight Benefits
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Environment
Reduction of aircraft emissions and effects of global warming.
Notes: For Air cargo carriers:
– Cargo carriers save money
– Reduced prices capture market share, increase profit
– Increased range reaches additional markets, more profit

## Slide 45: Formation Flight Case Stuydy
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Notes: Why now?
– New advances in software and GPS have enabled position- keeping
• NASA AFF program
– World air cargo traffic growing on average 6.4% per year in the next 20 years
• Asian market growing at 10.3%
– Fuel prices increasing (44% over the past year) • Demand for technology to lower fuel costs • Fuel costs normally 12-18% of total airline costs

## Slide 46: Formation Flight Types
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Source: Andrew Ning

## Slide 47: Formation Flight made possible through Datalink by…
Providing pilot information on probability of collisions and when to resume control when on autopilot.
Device can be sensory such as a Head Mounted Display.
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Source:NAMRL

## Slide 48: Formation Flight made possible through Datalink by…
Each aircraft determines it’s own position via GPS and sends information to other aircraft via pilot to pilot datalink
Wireless datalink to determine if an aircraft is within range of formation
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm

## Slide 49: Formation Flight Takeoff
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Source: MIT

## Slide 50: Formation Flight Join-up
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Source: MIT

## Slide 51: Formation Flight Breakaway
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Source: MIT

## Slide 52: Autonomous Formation Flight (AFF) System Architecture
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm

## Slide 53: Datalink and Differential GPS for Position Sensing
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Source: NASA

## Slide 54: VDL Mode 4 supporting surveillance
Cockpit display
CDTI
Position reports
ADS-B
Air Traffic Control
Notes: In an ADS-B system each aircraft/vehicle is periodically broadcasting position and additional information. These transmissions are available for everyone who are properly equipped, i.e surrounding aircraft/vehicles, ATC and AOC centres. The received information is typically displayed on Cockpit Display Traffic Display (CDTI) in cockpit giving pilots information on the situation surrounding their own aircraft. The position data is also typically presented on controller’s displays.

## Slide 55: Cockpit display (CDTI) – airborne situation
Gives pilot a display of
surrounding traffic

## Slide 56: Cost/Benefit Analysis
Variable | Advantages | Drawbacks
↑ precision | ↓ drag | ↑ cost
↑ system integration level | ↑ precision | ↑ cost ,↑ risk ↑ development time
↑ new technologies | ↑ precision | ↑ risk, ↑ cost
↑ no. of aircraft in formation | ↓ drag ↓ congestion | ↑ ATC separation ↓ string stability ↑ controller workload
↑ types and no. of aircraft certified to fly in formation | ↑ operational flexibility | ↑ size of test matrix ↑ mapping matrix ↑ time to certify
↑ ATC separation buffer | ↑ safety | ↑ congestion

## Slide 57: Datalink Control Architecture
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm
Centralized Leader-Follower:
  Has single leader plane within the formation that issues commands to all other aircraft
  Leader:
    Receives relative and absolute state information from all other planes
    Acts as DGPS base station
    Issues commands designed to:
      Maintain formation shape with other planes
      Anticipate future planned maneuvers and changes.
Followers:
  Receives state communication from leader and calculates to execute.
  Sends aircraft state info to leader.

## Slide 58: Emerging Services: Next Steps for us
Tailored Arrivals
  Optimized arrival profile up-linked to aircraft and loaded into FMS
Waypoint Management
  Managed in-flight spacing using Data Comm for delivery of control times at strategic points
4-D Trajectory Optimization
  Enhancements to flight profiles are negotiated via CPDLC
ADS-C Oceanic In-Trail Procedures
  Separation down to 15NM for climb and descent through a blocking aircraft, and
Background | Problem | DataLink| Applications| Case Study| Future
FutureComm

## Slide 59
Next Steps:
Tailored Arrivals.
Continuous Descent Approaches (CDA) and (Required Time of Arrival – RTA’s ) commmunicated through datalink.

## Slide 60: Segregated Information Broadcast (SIB)
By: Jeff Ma

## Slide 61: The Party line Effect
Radio Communication
Benefit of Eavesdropping
Datalink
Loss of situational awareness

## Slide 62: Situational Awareness

## Slide 63: SIB by Sectors

## Slide 64: SIB by Sectors

## Slide 65: SIB by Groups
Flight Formation
(1800) ATC: Southwest79 to join formation. Accept?
(1802) Southwest79 Accepts.
(1802) ATC: Increase speed by 10 knots and turn 5 degrees to the right.
ATC receives automated msg when pilot complete manuever
ATC: Decrease Elevation by 500meters
ATC receives automated msg when pilot complete manuever
…

## Slide 66: SIB by Destination
http://www.flightstats.com/go/FlightStatus/flightStatusByAirport.do

## Slide 67: SIB by Destination: Airport Witholding Procedure

## Slide 68: SIB
Summary and Benefits
Situational Awareness of Pilots
Fuel savings

## Slide 69: Conclusion
DataComm has many unique advantages, but also many challenges associated
Change in National Air System is more “evolution than revolution” (F. Ketcham)
Continual Development of innovative ideas to further NextGen
Continual research into NextGen enablers to improve current system

## Slide 70
Thank you! Questions?